## Slide 1
Learning to Dispatch for Job Shop Scheduling via Deep Reinforcement Learning
Contributions
A novel reinforcement learning (RL) algorithm for learning priority dispatching rules (PDRs) for job-shop scheduling problem (JSSP).
We show how PDRs with strong performance and effective generalization can be learned by using a graph-based MDP formulation and a RL agent.
Figure 1:Disjunctive graph representation.
Cong Zhang1, Wen Song2, Zhiguang Cao3, Jie Zhang1, Puay Siew Tan4, and Chi Xu4
1Nanyang Technological University, 2Institute of Marine Science and Technology, Shandong University, China, 3National University of Singapore, 4Singapore Institute of Manufacturing Technology, A*STAR
Background
Job-Shop Scheduling Problem (JSSP):
A set of jobs, where has operations .
Machines set
A predefined processing order , .
Objective: , and is starting time of .
(a): JSSP instance
(b): Complete solution
Motivation
However, the design of effective PDRs is a tedious task:
Requiring a myriad of specialized knowledge.
Delicate and limited performance for different JSSP.
Q:How to search the PDR space automatically to find PDRs that have robust generalization and strong performance?
Priority Dispatching Rules (PDRs): a class of heuristics that is widely used to solve real-world JSSP. Based on some calculated priority indices, it dispatches and schedules, within the current waiting list, the operation with highest priority index.
Markov Decision Process (MDP) Formulation
Experiments
State Transition:
1. Find the earliest feasible time period to allocate on the required machine;
2. Allocate in that period;
3. Update the directions of the disjunctive arcs of that machine;
In this way: we build the tight schedule. An example in Figure 2.
Figure 2: Example of state transition. Orange nodes are operations already scheduled, and the grey node is operation selected to be scheduled at current state. Integers in bracket are starting time of scheduled operations, where unscheduled operations have unknown starting time (denoted as?).
Parameterizing the Policy
Graph Embedding: We use Graph Isomorphism Network (GIN) as the embedding network, where at each layer the embedding can be formulated as:
  is the set of neighbors of node in the underline graph.
  To generalize GIN to support disjunctive graphs, which is originally proposed for undirected graphs, we propose a so-called ‘adding-edge’ strategy: new conjunctive arcs are added to next state based on action during transition, where all disjunctive arcs are neglected, as shown in Figure 3.
Figure 3: Example of state transition with left-shifting and adding-edge strategy. Orange nodes are operations already scheduled, and the grey node is operation selected to be scheduled at current state. Integers in bracket are starting time of scheduled operations, where unscheduled operations have unknown starting time (denoted as?).
Training Algorithm: Proximal Policy Optimization (PPO) as training algorithm.
Dataset: Synthetic dataset, Taillard’s instances (open), DMU instances (open)
Baselines: 4 Strong hand-designed rules from literature
Result: only results for Taillard’s instances and DMU instances are showed here due to limited space.
Table 1: Results on Taillard’s instances and DMU instances. ‘Gap’ is calculated against results obtained by OR-Tools with cut-off 3600 seconds. "Opt. Rate": rate of instances with optimal solution.
Disjunctive Graph (DG): , an example is Figure 1.
Node set : , , , denoting the start and terminal.
Conjunction set : directed arcs representing precedent constrains.
Disjunction set : undirected arcs connecting operations on the same machine.
Solution of JSSP: fixing the direction of each disjunction .
State: disjunctive graph representing current solution.
: directed disjunctive arcs that have been assigned a direction till . . and are DGs representing initial state (original JSSP) and complete solution where .
Action: is an eligible operation at time .
Reward: , is the lower bound of 𝐶_𝑚𝑎𝑥.
Note in Figure 2, it can be found that has a earliest feasible period between and , so is allocated in between them rather than being a successor of . The starting time of also changes from 7 (in ) to 11 (in ) accordingly.
paper
Policy network: A MLP
Critic network: A MLP
Policy and critic share the embedding network, and the whole architecture is depicted by Figure 4.
Figure 4. Actor-Critic Architecture